## Slide 1
When usage exceeds capacity
Each GCell edge has capacity two on tiny_gr
learn_global_routing — 01 edge overflow
Notes: Each GCell edge has capacity two on tiny_gr. Every routed net deposits plus one on each edge it uses. Overflow is how far usage exceeds capacity—summed, maxed, and counted per edge.

## Slide 2
The idea
For each edge e, overflow e equals max of zero and usage e minus capacity
Total is the sum across edges
Max is the worst edge
Count is how many edges have positive overflow
Sequential L-HV on all six nets should yield positive total overflow at cap two
learn_global_routing — 01 edge overflow
Notes: For each edge e, overflow e equals max of zero and usage e minus capacity. Total is the sum across edges. Max is the worst edge. Count is how many edges have positive overflow. Sequential L-HV on all six nets should yield positive total overflow at cap two.

## Slide 3
Overflow
Overflow
learn_global_routing — 01 edge overflow
Notes: ov(e)=max(0, usage(e)−Cap) per edge.

## Slide 4
Total overflow
Total overflow
learn_global_routing — 01 edge overflow
Notes: Sum over edges—primary regression scalar.

## Slide 5
Max overflow
Max overflow
learn_global_routing — 01 edge overflow
Notes: Worst edge—catches hotspot corridors.

## Slide 6
Overflow count
Overflow count
learn_global_routing — 01 edge overflow
Notes: How many edges exceed Cap.

## Slide 7
Hit targets
Hit targets
learn_global_routing — 01 edge overflow
Notes: Move pins or switch HV/VH/maze to clear thresholds.

## Slide 8
Browser lab track
Browser lab starter
learn_global_routing — 01 edge overflow
Notes: Open **edge-overflow**. Run sequential L routes and read the triple total max count. Heat-map the worst edge.

## Slide 9
Implement track
Implement `edge_overflow(usage, capacity)`
Call route_nets with mode l_hv on tiny_gr and assert total overflow is greater than zero
learn_global_routing — 01 edge overflow
Notes: Implement `edge_overflow(usage, capacity)`. Call route_nets with mode l_hv on tiny_gr and assert total overflow is greater than zero.

## Slide 10
Pitfalls
Computing overflow before summing all nets
Using tile demand from congestion instead of edge usage
Reporting negative overflow values
learn_global_routing — 01 edge overflow
Notes: Computing overflow before summing all nets. Using tile demand from congestion instead of edge usage. Reporting negative overflow values.

## Slide 11
Your turn
Hit overflow targets
Next: rip-up the hottest net and maze reroute
learn_global_routing — 01 edge overflow
Notes: Hit overflow targets. Next: rip-up the hottest net and maze reroute.