## Slide 1
Terminal propagation
Pads and fixed I/O pin nodes to sides before free cells move
learn_partitioning — 03 terminal propagation
Notes: Pads and fixed I/O pin nodes to sides before free cells move. Terminal propagation carries those constraints into the partition so the cut respects the chip boundary. Pin A to one side and E to the other and watch which free nodes follow.

## Slide 2
The idea
Fixed terminals never flip
Their neighbors inherit a pull toward the terminal’s part
Ignoring terminals produces pretty cuts that violate the floorplan interface
<!-- algorithm-walkthrough -->
learn_partitioning — 03 terminal propagation
Notes: Fixed terminals never flip. Their neighbors inherit a pull toward the terminal’s part. Ignoring terminals produces pretty cuts that violate the floorplan interface—illegal in real flows.
<!-- algorithm-walkthrough -->

## Slide 3
Fix pads A and E to opposite sides
Fix pads A and E to opposite sides
learn_partitioning — 03 terminal propagation
Notes: I/O terminals are pinned: A→side 0, E→side 1. Free nodes B, C, D propagate by taking the side of the strongest neighboring fixed/assigned node.

## Slide 4
B joins A (w=5)
B joins A (w=5)
learn_partitioning — 03 terminal propagation
Notes: B hears A strongly on side 0 (A–B weight 5) versus weak pull from E. B adopts side 0 immediately.

## Slide 5
D joins E (w=5)
D joins E (w=5)
learn_partitioning — 03 terminal propagation
Notes: D hears E on side 1 (D–E weight 5). D adopts side 1, forming the DE block opposite ABC.

## Slide 6
C bridges by neighbor vote
C bridges by neighbor vote
learn_partitioning — 03 terminal propagation
Notes: C connects to both communities. Neighbor vote sums favor joining A/B side (w=4+1 vs w=2+1). C lands on side 0 with A,B.

## Slide 7
Fixed I/O drives partition
Fixed I/O drives partition
learn_partitioning — 03 terminal propagation
Notes: Terminal propagation converges in 2 iterations on this graph. Real designs pin hundreds of pads — free logic follows connectivity to terminals.
<!-- /algorithm-walkthrough -->

## Slide 8
Browser lab track
In the browser lab track, open the terminal-propagation lab from the tools shelf
Load the starter graph, run the algorithm once
Work the challenges that lock the goldens
learn_partitioning — 03 terminal propagation
Notes: In the browser lab track, open the **terminal-propagation** lab from the tools shelf. Load the starter graph, run the algorithm once, and read cutsize and balance in the metrics panel. Work the challenges that lock the goldens, then come back to implement the same loop yourself.

## Slide 9
Implement track
In the implement track, open this module’s examples and the course `common/` solvers
Parse the tiny graph, run the algorithm with a deterministic seed
Match the browser goldens before you claim the checklist
learn_partitioning — 03 terminal propagation
Notes: In the implement track, open this module’s examples and the course `common/` solvers. Parse the tiny graph, run the algorithm with a deterministic seed, and print the assignment plus cutsize and balance. Match the browser goldens before you claim the checklist.

## Slide 10
Pitfalls
Common traps
For multilevel flows, verify coarsening before you blame the refiner
learn_partitioning — 03 terminal propagation
Notes: Common traps: optimizing cut while ignoring balance; reporting pairwise cut when the instance is a hypergraph; flipping locked terminals; and stopping before rollback to the best KL or FM prefix. For multilevel flows, verify coarsening before you blame the refiner.

## Slide 11
Your turn
Complete the checklist for at least one track, preferably both
Implement until your metrics match the starter goldens
When you’re ready, take the short quiz, then continue to the next module
learn_partitioning — 03 terminal propagation
Notes: Complete the checklist for at least one track—preferably both. Implement until your metrics match the starter goldens. When you’re ready, take the short quiz, then continue to the next module.