## Slide 1
Why GCells
After legalization you have legal cell sites, but routers still think in coarser tiles called GCells
learn_congestion — 01 gcell grid
Notes: After legalization you have legal cell sites, but routers still think in coarser tiles called GCells. Our toy chip is twelve by eight. We overlay a four by two grid: each GCell is three wide and four tall. Congestion literacy starts by naming which tile owns a point.

## Slide 2
The idea
Index with lower-left origin
Column i is floor of x over cell width, clamped to zero through three
Row j is floor of y over cell height, clamped to zero or one
Cell A at one comma one lands in GCell zero comma zero
Cell D at eight comma five lands in two comma one
Memorize that mapping, every estimator reuses it
learn_congestion — 01 gcell grid
Notes: Index with lower-left origin. Column i is floor of x over cell width, clamped to zero through three. Row j is floor of y over cell height, clamped to zero or one. Cell A at one comma one lands in GCell zero comma zero. Cell D at eight comma five lands in two comma one. Memorize that mapping—every estimator reuses it.

## Slide 3
Chip and GCells
Chip and GCells
learn_congestion — 01 gcell grid
Notes: Twelve by eight chip with a four-by-two GCell overlay. Each tile is three by four.

## Slide 4
A lands in (0,0)
A lands in (0,0)
learn_congestion — 01 gcell grid
Notes: Cell A at (1,1) indexes to GCell column 0, row 0.

## Slide 5
D lands in (2,1)
D lands in (2,1)
learn_congestion — 01 gcell grid
Notes: D at (8,5) → i=2, j=1 (top row).

## Slide 6
Paint all centers
Paint all centers
learn_congestion — 01 gcell grid
Notes: Every cell maps to exactly one GCell; the grid is the router’s coarse map.

## Slide 7
Clustered seed
Clustered seed
learn_congestion — 01 gcell grid
Notes: Congested seed piles cells into center tiles—later labs heat those GCells.

## Slide 8
Browser lab track
Browser lab starter
learn_congestion — 01 gcell grid
Notes: Open the **gcell-grid** lab. Move a cell and read the GCell index in the metrics panel. Paint the grid lines so the four-by-two tiling is obvious. Then encode the same clamp-and-floor rule in Track A.

## Slide 9
Implement track
Parse `tiny_cong.json`
Print nx, ny, cellW, cellH
Write `cell_gcell(x, y)` returning (i, j)
Assert A→(0,0) and D→(2,1) on the spread placement
No demand yet, this module is pure geometry
learn_congestion — 01 gcell grid
Notes: Parse `tiny_cong.json`. Print nx, ny, cellW, cellH. Write `cell_gcell(x, y)` returning (i, j). Assert A→(0,0) and D→(2,1) on the spread placement. No demand yet—this module is pure geometry.

## Slide 10
Pitfalls
Using upper-left image coordinates instead of chip lower-left
Forgetting to clamp points on the right or top edge into the last tile
Mixing site columns from legalization with GCell columns, different grids
learn_congestion — 01 gcell grid
Notes: Using upper-left image coordinates instead of chip lower-left. Forgetting to clamp points on the right or top edge into the last tile. Mixing site columns from legalization with GCell columns—different grids.

## Slide 11
Your turn
Finish the checklist
Be able to sketch the eight GCells from memory
Next: capacity versus demand, the supply side of the map
learn_congestion — 01 gcell grid
Notes: Finish the checklist. Be able to sketch the eight GCells from memory. Next: capacity versus demand—the supply side of the map.