## Slide 1
Fixed macros
Macro D is locked at (8, 4) on the top row, width two blocks sites eight and nine
learn_legalization — 01 fixed macros
Notes: Macro D is locked at (8, 4) on the top row—width two blocks sites eight and nine. Run Abacus with fixed macros: D never moves, movables pack around the obstacle, and the run stays legal with displacement four on this instance.

## Slide 2
The idea
Fixed cells are placed first; occupied intervals block shelf and Abacus trials on that row
Legality adds a macro check, any drift off the lock fails
Movable cells must route around macro sites, not slide through them
<!-- algorithm-walkthrough -->
learn_legalization — 01 fixed macros
Notes: Fixed cells are placed first; occupied intervals block shelf and Abacus trials on that row. Legality adds a macro check—any drift off the lock fails. Movable cells must route around macro sites, not slide through them.
<!-- algorithm-walkthrough -->

## Slide 3
Macro D locked at (8, 4)
Macro D locked at (8, 4)
learn_legalization — 01 fixed macros
Notes: Cell D is a fixed macro at (8, 4) on the top row—width two covers sites eight and nine. Every legalizer must leave D untouched while packing movables around it.

## Slide 4
Abacus with fixed macros
Abacus with fixed macros
learn_legalization — 01 fixed macros
Notes: Run Abacus with the fixed map: D is placed first, occupied sites on row four block C from sliding into the macro. Movable cells trial rows respecting blocked intervals.

## Slide 5
D never moves
D never moves
learn_legalization — 01 fixed macros
Notes: After Abacus with fixed macros, D remains at (8, 4). Legality report includes a macro check—any drift off the lock fails the run.

## Slide 6
Still legal, displacement 4
Still legal, displacement 4
learn_legalization — 01 fixed macros
Notes: With D fixed, Abacus still legalizes A, B, C, E, and F with total displacement four—the same as the unconstrained Abacus run on this instance because D never moved in either.

## Slide 7
Movables avoid macro sites
Movables avoid macro sites
learn_legalization — 01 fixed macros
Notes: C lands on row four at x four—left of E at zero, right of the macro gap. Packing algorithms must treat fixed macros as obstacles, not soft preferences.
<!-- /algorithm-walkthrough -->

## Slide 8
Browser lab track
In the browser lab track, open the fixed-macros lab from the tools shelf
Load the overlap or float starter, run the legalizer once
Work the challenges that lock the goldens
learn_legalization — 01 fixed macros
Notes: In the browser lab track, open the **fixed-macros** lab from the tools shelf. Load the overlap or float starter, run the legalizer once, and read legality plus displacement and HPWL when the panel shows them. Work the challenges that lock the goldens, then come back to implement the same loop yourself.

## Slide 9
Implement track
In the implement track, open this module's examples and the course `common/` solvers
Parse `tiny_legal.json`, run the algorithm with deterministic coordinates
Match the browser goldens before you claim the checklist
learn_legalization — 01 fixed macros
Notes: In the implement track, open this module's examples and the course `common/` solvers. Parse `tiny_legal.json`, run the algorithm with deterministic coordinates, and print legality, displacement, and HPWL. Match the browser goldens before you claim the checklist.

## Slide 10
Pitfalls
Common traps
learn_legalization — 01 fixed macros
Notes: Common traps: assuming snap alone legalizes; forgetting site width when checking overlap; ignoring fixed macro D at (8, 4); reporting HPWL without legality; and comparing Abacus and Tetris without naming displacement versus wirelength tradeoffs.

## Slide 11
Your turn
Complete the checklist for at least one track, preferably both
Implement until your metrics match the starter goldens
When you're ready, take the short quiz, then continue to the next module
learn_legalization — 01 fixed macros
Notes: Complete the checklist for at least one track—preferably both. Implement until your metrics match the starter goldens. When you're ready, take the short quiz, then continue to the next module.