## Slide 1
Layer changes at bends
Real detailed routes switch between M1 and M2 at vias
learn_routing — 07 via assignment
Notes: Real detailed routes switch between M1 and M2 at vias. Our L-route with layers walks horizontal on M1 and vertical on M2—or the VH variant—and marks via equals true at the bend cell.

## Slide 2
The idea
Given start and goal
L_route_layers returns segment dicts with x y layer and optional via flag
A path from one comma one to five comma four in HV includes at least one via
learn_routing — 07 via assignment
Notes: Given start and goal, prefer HV walks horizontal on M1 to align columns, inserts a via segment at the bend, then walks vertical on M2. l_route_layers returns segment dicts with x y layer and optional via flag. A path from one comma one to five comma four in HV includes at least one via.

## Slide 3
L-bend via
L-bend via
learn_routing — 07 via assignment
Notes: Layered L places a via at the corner to switch M1→M2.

## Slide 4
A–C example
A–C example
learn_routing — 07 via assignment
Notes: Spread A–C layered path uses M1 then M2 with via.

## Slide 5
Canvas vias
Canvas vias
learn_routing — 07 via assignment
Notes: Walkthrough marks via points on the grid.

## Slide 6
Multi-pin
Multi-pin
learn_routing — 07 via assignment
Notes: Four-pin net concatenates L legs—multiple vias possible.

## Slide 7
Spacing next
Spacing next
learn_routing — 07 via assignment
Notes: Vias do not replace DRC spacing checks.

## Slide 8
Browser lab track
Browser lab starter
learn_routing — 07 via assignment
Notes: Open **via-assignment**. Route A to B with HV and read via markers in the segment list. Toggle VH on the same pair and compare the bend cell and layers.

## Slide 9
Implement track
Implement `l_route_layers(a, b, prefer)`
Route net A–B on tiny_dr and print segments with via flags
Match the browser overlay
learn_routing — 07 via assignment
Notes: Implement `l_route_layers(a, b, prefer)`. Route net A–B on tiny_dr and print segments with via flags. Match the browser overlay.

## Slide 10
Pitfalls
Skipping the via marker at the bend
Putting horizontal motion on M2 or vertical on M1
Forgetting the final segment must land on the goal coordinates
learn_routing — 07 via assignment
Notes: Skipping the via marker at the bend. Putting horizontal motion on M2 or vertical on M1. Forgetting the final segment must land on the goal coordinates.

## Slide 11
Your turn
Ship Track A layer routes with vias
Next: DRC spacing lite on parallel tracks
learn_routing — 07 via assignment
Notes: Ship Track A layer routes with vias. Next: DRC spacing lite on parallel tracks.