## Slide 1
Fiduccia–Mattheyses refinement
FM refines a bipartition with single-vertex moves, locking
learn_clustering — 07 fiduccia mattheyses
Notes: FM refines a bipartition with single-vertex moves, locking, and rollback—cousin to Kernighan–Lin, but one cell at a time. On the same bad seed that starts at cutsize twelve, FM reaches cutsize three.
<!-- algorithm-walkthrough -->

## Slide 2
Same bad seed, different move set
Same bad seed, different move set
learn_clustering — 07 fiduccia mattheyses
Notes: FM starts from the same cutsize-twelve seed, but moves one vertex at a time instead of swapping a pair. That suits hypergraph and cell-move implementations.

## Slide 3
Move 1: flip D (gain 3)
Move 1: flip D (gain 3)
learn_clustering — 07 fiduccia mattheyses
Notes: Highest legal move sends D to the other side with gain three. Partial progress: D joins E’s side early. Lock D and update neighbor gains.

## Slide 4
Move 2: flip A (gain 6)
Move 2: flip A (gain 6)
learn_clustering — 07 fiduccia mattheyses
Notes: Next, A flips with gain six. Cumulative gain is three plus six—nine—the same total improvement KL found with one swap. Best k equals two keeps both moves.

## Slide 5
Final ABC|DE, cutsize 3
Final ABC|DE, cutsize 3
learn_clustering — 07 fiduccia mattheyses
Notes: FM lands on the same refined bipartition as KL. Move style differs; destination quality matches on this instance. Cutsize is three.

## Slide 6
Pass 1 confirms local optimum
Pass 1 confirms local optimum
learn_clustering — 07 fiduccia mattheyses
Notes: A second FM pass finds no improving move prefix. Stop. In real tools, FM often runs inside multilevel V-cycles with tighter balance and hyperedges.
<!-- /algorithm-walkthrough -->

## Slide 7
Browser lab track
In the browser lab, show the seed, run FM, and compare the move list with KL’s single swap
Clear the challenges for twelve-to-three and the D-then-A prefix
learn_clustering — 07 fiduccia mattheyses
Notes: In the browser lab, show the seed, run FM, and compare the move list with KL’s single swap. Clear the challenges for twelve-to-three and the D-then-A prefix.

## Slide 8
Implement track
Run FM on the shared bad seed
Confirm moves D then A in the accepted prefix, and cut twelve to three
Re-implement selection and rollback until tests pass
learn_clustering — 07 fiduccia mattheyses
Notes: Run FM on the shared bad seed. Confirm moves D then A in the accepted prefix, and cut twelve to three. Re-implement selection and rollback until tests pass.

## Slide 9
Implement track — try these
# FM refinement on the shared bad seed
export PYTHONPATH=../common
python ../common/solvers.py examples/tiny_graph.json --mode fm --seed
../module02-05-kernighan-lin/examples/seed_partition.json
learn_clustering — 07 fiduccia mattheyses

## Slide 10
Pitfalls to watch
Skipping rollback keeps a worse locked state
Ignoring balance lets one side empty
Stale gains after a move pick the wrong cell next
learn_clustering — 07 fiduccia mattheyses
Notes: Skipping rollback keeps a worse locked state. Ignoring balance lets one side empty. Stale gains after a move pick the wrong cell next.

## Slide 11
Your turn
Reproduce twelve to three
learn_clustering — 07 fiduccia mattheyses
Notes: Reproduce twelve to three, finish the checklist and quiz, then continue to multilevel clustering.