## Slide 1
Timing-aware clustering
Critical nets should stay uncut
learn_clustering — 03 timing aware clustering
Notes: Critical nets should stay uncut. You’ll watch FM on criticality-weighted edges and land on cutsize three with weighted cut seven—protecting the A–B–C path.
<!-- algorithm-walkthrough -->

## Slide 2
Mark critical edges
Mark critical edges
learn_clustering — 03 timing aware clustering
Notes: Criticality map emphasizes path A–B–C–D: A–B=5, B–C=4, C–D=3. Cutting critical edges hurts timing more than raw wire weight suggests.

## Slide 3
Reweight then refine
Reweight then refine
learn_clustering — 03 timing aware clustering
Notes: Multiply each edge by its criticality (default 1 if missing). FM now strongly prefers keeping A–B and B–C internal.

## Slide 4
Land on ABC|DE
Land on ABC|DE
learn_clustering — 03 timing aware clustering
Notes: Timing-aware FM reaches ABC|DE. Plain cutsize is 3; weighted cut (criticality-scaled) is 7.

## Slide 5
Critical edges uncut
Critical edges uncut
learn_clustering — 03 timing aware clustering
Notes: A–B and B–C stay inside ABC. The cut uses less critical bridges C–D and C–E — acceptable plain cut, better timing story.

## Slide 6
Timing as an objective
Timing as an objective
learn_clustering — 03 timing aware clustering
Notes: Reweighting turns the same FM kernel into a timing-aware partitioner. Students compare plain vs weighted metrics on one seed.
<!-- /algorithm-walkthrough -->

## Slide 7
Browser lab track
In the browser lab, run timing-aware refinement from the bad seed
Confirm plain cut three and weighted cut seven
learn_clustering — 03 timing aware clustering
Notes: In the browser lab, run timing-aware refinement from the bad seed. Confirm plain cut three and weighted cut seven.

## Slide 8
Implement track
Run timing-aware mode and confirm ABC versus DE, plain three, weighted seven
learn_clustering — 03 timing aware clustering
Notes: Run timing-aware mode and confirm ABC versus DE, plain three, weighted seven.

## Slide 9
Implement track — try these
export PYTHONPATH=../common
python ../common/solvers.py examples/tiny_graph.json --mode timing
--seed ../module02-05-kernighan-lin/examples/seed_partition.json
--criticality examples/criticality.json
learn_clustering — 03 timing aware clustering

## Slide 10
Pitfalls to watch
Criticality of one means no boost, document defaults
Mixing plain and weighted metrics in the same table confuses compares
learn_clustering — 03 timing aware clustering
Notes: Criticality of one means no boost—document defaults. Mixing plain and weighted metrics in the same table confuses compares.

## Slide 11
Your turn
Match the golden
learn_clustering — 03 timing aware clustering
Notes: Match the golden, finish the checklist and quiz, then continue to offline benchmark compare.