## Slide 1
Force-directed placement
Force-directed place pulls each free cell toward the average of its net neighbors, plus a weak center pull
learn_placement — 01 force directed place
Notes: Force-directed place pulls each free cell toward the average of its net neighbors, plus a weak center pull. From the starter HPWL of fifty-two, a few lite iterations land near eighteen point seven—better wirelength, still above the golden fourteen.

## Slide 2
The idea
Each iteration
Fixed pads stay put
Too much alpha collapses the design; too little barely moves
Report HPWL before and after with the same net model
<!-- algorithm-walkthrough -->
learn_placement — 01 force directed place
Notes: Each iteration: for free cells, blend current position toward the neighbor average with a small alpha. Fixed pads stay put. Too much alpha collapses the design; too little barely moves. Report HPWL before and after with the same net model.
<!-- algorithm-walkthrough -->

## Slide 3
Start from HPWL fifty-two
Start from HPWL fifty-two
learn_placement — 01 force directed place
Notes: Force-directed place pulls free cells toward the average of their net neighbors, plus a weak center pull. Begin on the spread starter at HPWL fifty-two.

## Slide 4
Neighbors pull cells inward
Neighbors pull cells inward
learn_placement — 01 force directed place
Notes: After a couple of lite iterations, A–D drift toward the center while E and F follow their neighbors. Wirelength is already dropping.

## Slide 5
After force: about eighteen point seven
After force: about eighteen point seven
learn_placement — 01 force directed place
Notes: Default five iterations land near eighteen point seven—clearly better than fifty-two, still above the compact golden fourteen.

## Slide 6
Force vs golden compact
Force vs golden compact
learn_placement — 01 force directed place
Notes: Golden fourteen is tighter still. Force is a cheap continuous move—good teaching progress without claiming the absolute minimum.

## Slide 7
Alpha trades speed vs collapse
Alpha trades speed vs collapse
learn_placement — 01 force directed place
Notes: Too much alpha stacks cells; too little barely moves. Lock the iteration count and alpha so your eighteen point seven golden stays stable.
<!-- /algorithm-walkthrough -->

## Slide 8
Browser lab track
In the browser lab track, open the force-directed-place lab from the tools shelf
Load the starter placement, run the algorithm once
Work the challenges that lock the goldens
learn_placement — 01 force directed place
Notes: In the browser lab track, open the **force-directed-place** lab from the tools shelf. Load the starter placement, run the algorithm once, and read HPWL—and density when the panel shows it. Work the challenges that lock the goldens, then come back to implement the same loop yourself.

## Slide 9
Implement track
In the implement track, open this module’s examples and the course `common/` solvers
Parse `tiny_place.json`, run the algorithm with a deterministic seed
Match the browser goldens before you claim the checklist
learn_placement — 01 force directed place
Notes: In the implement track, open this module’s examples and the course `common/` solvers. Parse `tiny_place.json`, run the algorithm with a deterministic seed, and print coordinates plus HPWL. Match the browser goldens before you claim the checklist.

## Slide 10
Pitfalls
Common traps
learn_placement — 01 force directed place
Notes: Common traps: celebrating HPWL while cells pile into one bin; ignoring fixed pads A and D; mixing bbox and clique models in one report; keeping only the final SA iterate instead of the best; and forgetting that timing weights change the objective, not just the label.

## Slide 11
Your turn
Complete the checklist for at least one track, preferably both
Implement until your metrics match the starter goldens
When you’re ready, take the short quiz, then continue to the next module
learn_placement — 01 force directed place
Notes: Complete the checklist for at least one track—preferably both. Implement until your metrics match the starter goldens. When you’re ready, take the short quiz, then continue to the next module.