## Slide 1
Slack, setup, and hold
Slack turns tags into a pass or fail
learn_sta — 01 slack setup hold
Notes: Slack turns tags into a pass or fail. Setup slack is required minus arrival; hold uses a different required. You will get setup slack six point eight and hold slack three point two at out on the lite model.

## Slide 2
Goldens to remember
Setup: R−A = 10−3.2 = 6.8
Hold lite: A−0 = 3.2
Positive means the check passes
Keep these numbers handy, the browser challenges and Track A tests use the same instance
<!-- algorithm-walkthrough -->
learn_sta — 01 slack setup hold
Notes: Setup: R−A = 10−3.2 = 6.8. Hold lite: A−0 = 3.2. Positive means the check passes. Keep these numbers handy—the browser challenges and Track A tests use the same instance.
<!-- algorithm-walkthrough -->

## Slide 3
Setup slack is required minus arrival
Setup slack is required minus arrival
learn_sta — 01 slack setup hold
Notes: At the endpoint out, setup slack equals R − A. With R=10 and A=3.2, slack is 6.8—positive means the path meets the single-cycle check.

## Slide 4
Hold slack uses a different required
Hold slack uses a different required
learn_sta — 01 slack setup hold
Notes: For this lite hold model, required at out is 0 on the same edge. Hold slack is A − R_hold = 3.2 − 0 = 3.2.

## Slide 5
The sign tells you pass or fail
The sign tells you pass or fail
learn_sta — 01 slack setup hold
Notes: Negative setup slack means the path is too slow for the period. Negative hold means data changes too soon. Read the sign before you chase the path.

## Slide 6
Report slack at endpoints first
Report slack at endpoints first
learn_sta — 01 slack setup hold
Notes: Engineers scan worst negative slack at endpoints, then open the path. On this toy netlist there is one sink—out—so both checks live there.

## Slide 7
Period changes setup, not hold lite
Period changes setup, not hold lite
learn_sta — 01 slack setup hold
Notes: If the period were tighter, setup required would drop and setup slack would shrink. Hold in this lite model stays tied to arrival versus zero.
<!-- /algorithm-walkthrough -->

## Slide 8
Browser lab track
In the browser lab, open slack-setup-hold
Load the starter, run the analysis once, and read the metrics panel
Orient yourself, challenge panel, canvas, Check, then mirror the same goldens in code
learn_sta — 01 slack setup hold
Notes: In the browser lab, open **slack-setup-hold**. Load the starter, run the analysis once, and read the metrics panel. Orient yourself—challenge panel, canvas, Check—then mirror the same goldens in code.

## Slide 9
Implement track
In the implement track
Run `python3 common/test_propagate.py` (and the timing-graph test) until the goldens print
learn_sta — 01 slack setup hold
Notes: In the implement track, use `common/tiny_timing.json` with the helpers in `common/graph.py` and `common/propagate.py`. Run `python3 common/test_propagate.py` (and the timing-graph test) until the goldens print ok.

## Slide 10
Pitfall
Do not mix setup and hold required maps
Do not propagate before the graph is levelized
After an edit or exception, recompute, stale tags lie
learn_sta — 01 slack setup hold
Notes: Do not mix setup and hold required maps. Do not propagate before the graph is levelized. After an edit or exception, recompute—stale tags lie.

## Slide 11
Your turn
Finish the checklist on at least one track, preferably both
When your numbers match the goldens, take the quiz, then continue
learn_sta — 01 slack setup hold
Notes: Finish the checklist on at least one track—preferably both. When your numbers match the goldens, take the quiz, then continue.