## Slide 1
Incremental timing update
Real timers cannot rebuild the chip after every buffer insert
learn_sta — 01 incremental update
Notes: Real timers cannot rebuild the chip after every buffer insert. They invalidate a cone and recompute. You will bump u1’s cell delay from 1.2 to 2.0 and see A(out) move from 3.2 to 4.0 with setup slack 6.0.

## Slide 2
Goldens to remember
Invalidated cone: u1/Y, u2/A, u2/Y, out
Clean: in, u1/A
ΔA(out)=+0.8
Keep these numbers handy, the browser challenges and Track A tests use the same instance
<!-- algorithm-walkthrough -->
learn_sta — 01 incremental update
Notes: Invalidated cone: u1/Y, u2/A, u2/Y, out. Clean: in, u1/A. ΔA(out)=+0.8. Keep these numbers handy—the browser challenges and Track A tests use the same instance.
<!-- algorithm-walkthrough -->

## Slide 3
Start from a full analysis
Start from a full analysis
learn_sta — 01 incremental update
Notes: Base arrival at out is 3.2 with setup slack 6.8. Incremental update never starts from an empty graph—it starts from valid tags.

## Slide 4
Edit one cell delay
Edit one cell delay
learn_sta — 01 incremental update
Notes: Bump the u1 cell arc from 1.2 to 2.0. Only the fanout cone of u1/Y can change—everything upstream of the edit stays put.

## Slide 5
Invalidate the fanout cone
Invalidate the fanout cone
learn_sta — 01 incremental update
Notes: Mark u1/Y, u2/A, u2/Y, and out dirty. Do not touch in or u1/A—their arrivals are still valid.

## Slide 6
Recompute only the dirty pins
Recompute only the dirty pins
learn_sta — 01 incremental update
Notes: Replay topo order on dirty pins. Arrival at out becomes 4.0; setup slack drops to 6.0. Same answer as a full rebuild, less work.

## Slide 7
Why timers insist on incremental
Why timers insist on incremental
learn_sta — 01 incremental update
Notes: Place, CTS, and ECO change tiny regions millions of times. Full-chip rebuilds every edit would not finish. Cone invalidate-and-repair is the habit.
<!-- /algorithm-walkthrough -->

## Slide 8
Browser lab track
In the browser lab, open incremental-update
Load the starter, run the analysis once, and read the metrics panel
Orient yourself, challenge panel, canvas, Check, then mirror the same goldens in code
learn_sta — 01 incremental update
Notes: In the browser lab, open **incremental-update**. Load the starter, run the analysis once, and read the metrics panel. Orient yourself—challenge panel, canvas, Check—then mirror the same goldens in code.

## Slide 9
Implement track
In the implement track
Run `python3 common/test_propagate.py` (and the timing-graph test) until the goldens print
learn_sta — 01 incremental update
Notes: In the implement track, use `common/tiny_timing.json` with the helpers in `common/graph.py` and `common/propagate.py`. Run `python3 common/test_propagate.py` (and the timing-graph test) until the goldens print ok.

## Slide 10
Pitfall
Do not mix setup and hold required maps
Do not propagate before the graph is levelized
After an edit or exception, recompute, stale tags lie
learn_sta — 01 incremental update
Notes: Do not mix setup and hold required maps. Do not propagate before the graph is levelized. After an edit or exception, recompute—stale tags lie.

## Slide 11
Your turn
Finish the checklist on at least one track, preferably both
When your numbers match the goldens, take the quiz, then continue
learn_sta — 01 incremental update
Notes: Finish the checklist on at least one track—preferably both. When your numbers match the goldens, take the quiz, then continue.